## Slide 1: Introduction to CUDA – A Workshop
Shehzan Mohammed
Lecturer, CIS 565 – GPU Programming & Architecture
University of Pennsylvania

## Slide 2: Today We’ll Learn
Intro to CUDA
Thread Hierarchy
Memory Model
Warps, Thread Scheduling, Synchronization
CUDA Examples:
  Vector Addition
  Matrix Multiply
CUDA Libraries

## Slide 3: Prerequisites
You (probably) need experience with C or C++
  Experience with pointers is even better
You don’t need GPU experience
You don’t need parallel programming experience
You don’t need graphics experience

## Slide 4: What is CUDA
CUDA Architecture
  Expose GPU parallelism for general-purpose computing
  Retain performance
CUDA C/C++
  Based on standard C/C++
  Small set of extensions to enable heterogenous programing
  Straightforward APIs to manage devices, memory, etc.

## Slide 5: GPU Computing History: APIs
2001/2002 – researchers see GPU as data-parallel coprocessor
  The GPGPU field is born
2007 – NVIDIA releases CUDA
  CUDA – Compute Uniform Device Architecture
  GPGPU shifts to GPU Computing
2008 – Khronos releases OpenCL specification
2013 – Khronos releases OpenGL compute shaders
2015 – Khronos releases Vulkan and SPIR-V
Notes: Compute shaders have been in Direct3D for a while.
WebCL never caught on.

## Slide 6: Heterogenous Computing - Terminology
Host: typically, the CPU
  Code written in C/C++ (or other languages)
Device: typically, the GPU (data-parallel)
  Code written in extended C/C++
Host and device have separate memories
  Except for SoC
CUDA Program
  Contains both host and device code
Host
Device

## Slide 7: Heterogenous Computing - Terminology
Kernel: data parallel function
  Invoking a kernel creates lightweight threads on the device
  Threads are generated and scheduled with hardware
Serial Code
Parallel Code
Serial Code

## Slide 8: Simple Processing Flow
Copy input data from CPU memory to GPU memory
PCI Bus

## Slide 9: Simple Processing Flow
Copy input data from CPU memory to GPU memory
Load GPU program and execute, caching data on chip for performance
PCI Bus

## Slide 10: Simple Processing Flow
Copy input data from CPU memory to GPU memory
Load GPU program and execute, caching data on chip for performance
Copy results from GPU memory to CPU memory
PCI Bus

## Slide 11: CUDA Kernels
Executed N times in parallel by N different CUDA threads
// Kernel Definition
__global__ void vectorAdd(const float* A, const float* B, float* C)
{
int i = threadIdx.x;
C[i] = A[i] + B[i];
}
int main()
{
// ....
// Kernel invocation with N threads
vectorAdd<<<1, N>>>(A, B, C);
}
Declaration specifier
Thread Index
Kernel execution configuration
Notes: threadIdx is a 3-component vector

## Slide 12: CUDA Program Execution
Image from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf

## Slide 13: Vector Addition
Goal: Add 2 x “N” Element Vectors

## Slide 14: Vector Addition - CPU
for(int i = 0; i < N; i++) {
c[i] = a[i] + b[i];
}

## Slide 15: Vector Addition - CPU
for(int i = 0; i < N; i++) {
c[i] = a[i] + b[i];
}
i=0

## Slide 16: Vector Addition - CPU
for(int i = 0; i < N; i++) {
c[i] = a[i] + b[i];
}
i=1

## Slide 17: Vector Addition - CPU
i=2
for(int i = 0; i < N; i++) {
c[i] = a[i] + b[i];
}

## Slide 18: Vector Addition - CPU
i=N-1
……
for(int i = 0; i < N; i++) {
c[i] = a[i] + b[i];
}

## Slide 19: Vector Addition
Can be done in parallel – no dependency!

## Slide 20: Vector Addition - CUDA
Executed N times in parallel by N different CUDA threads
// Kernel Definition
__global__ void vectorAdd(const float* A, const float* B, float* C)
{
int i = threadIdx.x;
C[i] = A[i] + B[i];
}
int main()
{
// ....
// Kernel invocation with N threads
vectorAdd<<<1, N>>>(A, B, C);
}
Declaration specifier
Thread Index
Kernel execution configuration
Notes: threadIdx is a 3-component vector

## Slide 21: Functional Declarations
 | Executed on the: | Only callable from the:
__global__ void KernelFunc() | device | host
__device__ float DeviceFunc() | device | device
__host__ float HostFunc() | host | host
See Appendix B.1 in the NVIDIA CUDA C Programming Guide for more details

## Slide 22: Functional Declarations
__global__
  Must return void
__device__
  Inlined by default
See Appendix B.1 in the NVIDIA CUDA C Programming Guide for more details

## Slide 23: Functional Declarations
What do these do?
__device__ __host__ void func()
__global__ __host__ void func()
See Appendix B.1 in the NVIDIA CUDA C Programming Guide for more details
Notes: Device + host = creates two functions
Global + host = not allowed.

## Slide 24: Functional Declarations
What do these do?
__device__ __host__ void func()
__global__ __host__ void func()
__host__ __device__ func ()
{
// …………
}
Code from http://developer.download.nvidia.com/compute/cuda/3_2_prod/toolkit/docs/CUDA_C_Programming_Guide.pdf
Notes: Use __CUDA_ARCH__ to know if code is for the host or device.

## Slide 25: Functional Declarations
Global and device functions
  Recursion allowed for device function
  No static variables
  No malloc()
Notes: Can’t take the address of a __device__ function in host code.
Can only call __device__ functions through pointers in compute capable 2.x.
No malloc as dynamic memory cannot be allocated at runtime - Use shared memory
G80 GLSL has similar constraints to GLSL

## Slide 26: Thread Hierarchies
Grid – one or more thread blocks
  1D, 2D or 3D
Block – array of threads
  1D, 2D, or 3D
  Each block in a grid has the same number of threads
  Each thread in a block can
    Synchronize
    Access shared memory

## Slide 27: Thread Hierarchies
Image from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf

## Slide 28: Thread Hierarchies - Block
1D, 2D, or 3D
  Example: Index into vector, matrix, volume

## Slide 29: Thread Hierarchies – Thread Id
Thread ID: Scalar thread identifier
Thread Index: threadIdx
1D: Thread ID == Thread Index
2D with size (Dx, Dy)
  Thread ID of index (x, y) == x + y Dx
3D with size (Dx, Dy, Dz)
  Thread ID of index (x, y, z) == x + y Dx + z Dx Dy

## Slide 30: Thread Hierarchies
// Kernel Definition
__global__ void matrixAddition(const float* A, const float* B, float* C)
{
int idx = threadIdx.y * blockDim.x + threadIdx.x;
C[idx] = A[idx] + B[idx];
}
int main()
{
// ....
// Kernel invocation with one block of N * N * 1 threads
int blocks = 1;
dim3 threadsPerBlock(N, N);
vectorAdd<<<blocks, threadsPerBlock>>>(A, B, C);
}
2D Thread Index to 1D memory index
1 block
2D block of threads
Notes: Using 2D so does not need to explicitly compute 1D thread ID from x and y

## Slide 31: Thread Hierarchies – Thread Block
Group of threads - Up to 1024 threads
Reside on the same SM
Share memory of that SM
Image from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf

## Slide 32: Thread Hierarchies
Block Index: blockIdx
Dimension: blockDim
  1D or 2D

## Slide 33: Thread Hierarchies
// Kernel Definition
__global__ void matrixAddition(const float* A, const float* B, float* C,
int N)
{
int x = blockIdx.x * blockDim.x + threadIdx.x;
int y = blockIdx.y * blockDim.y + threadIdx.y;
int idx = y * N + x;
C[idx] = A[idx] + B[idx];
}
int main()
{
// ....
// Kernel invocation with computed configuration
dim3 threadsPerBlock(16, 16);
dim3 blocks(N / threadPerBlock.x, N / threadPerBlock.y);
vectorAdd<<<blocks, threadsPerBlock>>>(A, B, C);
}
2D Thread Index to 1D memory index
2D grid of blocks
2D block of threads
16x16 Threads per Block
Notes: dim3 default argument is 1

## Slide 34: Thread Hierarchies
Example: N = 32 (Matrix = N rows x N columns)
16x16 threads per block (independent of N)
  threadIdx ([0, 15], [0, 15])
2x2 thread blocks in grid
  blockIdx ([0, 1], [0, 1])
  blockDim = 16
int i = blockIdx.x * blockDim.x + threadIdx.x;
int j = blockIdx.y * blockDim.y + threadIdx.y;

## Slide 35: Thread Hierarchies
Example: N=32 (Matrix = N rows x N columns)
16x16 threads per block (independent of N)
  threadIdx ([0, 15], [0, 15])
2x2 thread blocks in grid
  blockIdx ([0, 1], [0, 1])
  blockDim = 16
i = [0, 1] * 16 + [0, 15]
Min => i = 0 * 16 + 0 = 0
Max => i = 1 * 16 + 15 = 31
int i = blockIdx.x * blockDim.x + threadIdx.x;
int j = blockIdx.y * blockDim.y + threadIdx.y;
j = [0, 1] * 16 + [0, 15]
Min => j = 0 * 16 + 0 = 0
Max => j = 1 * 16 + 15 = 31

## Slide 36: Thread Hierarchies
Blocks execute independently
In any order: parallel or series
Scheduled in any order by any number of cores
  Allows code to scale with core count

## Slide 37: Thread Hierarchies
Image from: http://developer.download.nvidia.com/compute/cuda/3_2_prod/toolkit/docs/CUDA_C_Programming_Guide.pdf
Notes: Scheduled by the CUDA runtime

## Slide 38: Memory Management

## Slide 39: Memory Management
Host and device memory are separate entities
  Device pointers point to GPU memory
    May be passed to/from host code
    May not be dereferenced in host code
  Host pointers point to CPU memory
    May be passed to/from device code
    May not be dereferenced in device code
Simple CUDA API for handling device memory
  cudaMalloc(), cudaFree(), cudaMemcpy()
  Similar to the C equivalents malloc(), free(), memcpy()

## Slide 40: CUDA Memory Transfers
Image from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf

## Slide 41: CUDA Memory Transfers
Host can transfer to/from device
  Global memory
  Constant memory
Image from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf

## Slide 42: CUDA Memory Transfers
cudaMalloc()
  Allocate global memory on device
cudaFree()
  Frees memory
Image from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf

## Slide 43: CUDA Memory Transfers
float *deviceMemory = NULL;
int size = width * height * sizeof(float);
cudaMalloc((void**)&deviceMemory, size); // Allocate memory
// Do work
cudaFree(deviceMemory); // Free memory

## Slide 44: CUDA Memory Transfers
float *deviceMemory = NULL;
int size = width * height * sizeof(float);
cudaMalloc((void**)&deviceMemory, size); // Allocate memory
// Do work
cudaFree(deviceMemory); // Free memory
Pointer to device memory
Size in bytes

## Slide 45: CUDA Memory Transfers
cudaMemcpy()
  Host to host
  Host to device
  Device to host
  Device to device
Host
Device
Global Memory

## Slide 46: CUDA Memory Transfers
cudaMemcpy()
  Host to host
  Host to device
  Device to host
  Device to device
Host
Device
Global Memory

## Slide 47: CUDA Memory Transfers
cudaMemcpy()
  Host to host
  Host to device
  Device to host
  Device to device
cudaMemcpy(devicePtr, hostPtr, size, cudaMemcpyHostToDevice);
Destination (device)
Source (host)
Copy direction
Host
Device
Global Memory

## Slide 48: CUDA Memory Transfers
cudaMemcpy()
  Host to host
  Host to device
  Device to host
  Device to device
cudaMemcpy(hostPtr, devicePtr, size cudaMemcpyDeviceToHost);
Destination (host)
Source (device)
Copy direction
Host
Device
Global Memory

## Slide 49: CUDA Memory Transfers
cudaMemcpy()
  Host to host
  Host to device
  Device to host
  Device to device
Host
Device
Global Memory
cudaMemcpy(destPtr, srcPtr, size cudaMemcpyDeviceToDevice);
Destination (device)
Source (device)
Copy direction

## Slide 50: Vector Addition

## Slide 51: Vector Addition – Full CUDA Program
int main( int argc, char* argv[] ) {
// Size of vectors
int n = 100000;
// Host vectors
float *h_a, *h_b, *h_c;
// Device vectors
float *d_a, *d_b, *d_c;
// Size, in bytes, of each vector
size_t bytes = n*sizeof(float);
// Allocate memory for each vector on host
h_a = (float*)malloc(bytes);
h_b = (float*)malloc(bytes);
h_c = (float*)malloc(bytes);
// Allocate memory for each vector on GPU
cudaMalloc(&d_a, bytes);
cudaMalloc(&d_b, bytes);
cudaMalloc(&d_c, bytes);
// Initialize vectors on host
for(int i = 0; i < n; i++ ) {
h_a[i] = sin(i)*sin(i);
h_b[i] = cos(i)*cos(i);
}
// Copy host vectors to device
cudaMemcpy(d_a, h_a, bytes, cudaMemcpyHostToDevice);
cudaMemcpy(d_b, h_b, bytes, cudaMemcpyHostToDevice);
// Number of threads in each thread block
int blockSize = 1024;
// Number of thread blocks in grid
int gridSize = (int)ceil((float)n/blockSize);
// Execute the kernel
vecAdd<<<gridSize, blockSize>>>(d_a, d_b, d_c, n);
// Copy array back to host
cudaMemcpy(h_c, d_c, bytes, cudaMemcpyDeviceToHost);
// Release device memory
cudaFree(d_a); cudaFree(d_b); cudaFree(d_c);
// Release host memory
free(h_a); free(h_b); free(h_c);
return 0;
}

## Slide 52: Vector Addition – Full CUDA Program
// CUDA kernel. Each thread takes care of one element of c
__global__ void vecAdd(float *a, float *b, float *c, int n)
{
// Get our global thread ID
int id = blockIdx.x * blockDim.x + threadIdx.x;
// Make sure we do not go out of bounds
if (id < n)
c[id] = a[id] + b[id];
}

## Slide 53: Matrix Multiply

## Slide 54: Matrix Multiply Reminder
Vectors
Dot products
Row major or column major?
Dot product per output element

## Slide 55: Matrix Multiply
P = M * N
Assume M and N are square for simplicity
Image from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf

## Slide 56: Matrix Multiply
1,000 x 1,000 matrix
Anyone want to take a guess on the number of operations involved?
Notes: Or 999 adds depending on the code.

## Slide 57: Matrix Multiply: CPU Implementation
Code from: http://courses.engr.illinois.edu/ece498/al/lectures/lecture3%20cuda%20threads%20spring%202010.ppt
void MatrixMultiplyOnHost(float* M, float* N, float* P, int width)‏
{
for (int i = 0; i < width; ++i)‏
{
for (int j = 0; j < width; ++j)
{
float sum = 0;
for (int k = 0; k < width; ++k)
{
float a = M[i * width + k];
float b = N[k * width + j];
sum += a * b;
}
P[i * width + j] = sum;
}
}
}
Notes: Row major. The inner most loop goes across a row of M, and down a column of N.

## Slide 58: Matrix Multiply
1,000 x 1,000 matrix
  1,000,000 dot products
    Each 1,000 multiples and 1,000 adds
1 Billion multiplies and 1 Billion adds!!!
Notes: Or 999 adds depending on the code.

## Slide 59: Matrix Multiply: CUDA Skeleton
int main() {
// 1. Allocate and Initialize M, N, and result P matrices
// Copy M, N matrices to device
// 2. M * N on device
// 3. Copy P matrix to host and output
// Free device memory and clean up
return 0;
}

## Slide 60: Matrix Multiply
Step 1:
  Add CUDA memory transfers to the skeleton

## Slide 61: Matrix Multiply: Data Transfer
void MatrixMultiplyOnDevice(float* hostP, const float* hostM, const float* hostN, const int width)
{
int sizeInBytes = width * width * sizeof(float);
float *devM, *devN, *devP;
// Allocate M and N on device
cudaMalloc((void**)&devM, sizeInBytes);
cudaMalloc((void**)&devN, sizeInBytes);
// Allocate P
cudaMalloc((void**)&devP, sizeInBytes);
// Copy M and N from host to device
cudaMemcpy(devM, hostM, sizeInBytes, cudaMemcpyHostToDevice);
cudaMemcpy(devN, hostN, sizeInBytes, cudaMemcpyHostToDevice);
// Call the kernel here - Later
// Copy P matrix from device to host
cudaMemcpy(hostP, devP, sizeInBytes, cudaMemcpyDeviceToHost);
// Free allocated memory
cudaFree(devM); cudaFree(devN); cudaFree(devP);
}
Notes: Error in cudaMalloc calls: should pass address of point, e.g., “(void *)&Md”

## Slide 62: Matrix Multiply: Data Transfer
void MatrixMultiplyOnDevice(float* hostP, const float* hostM, const float* hostN, const int width)
{
int sizeInBytes = width * width * sizeof(float);
float *devM, *devN, *devP;
// Allocate M and N on device
cudaMalloc((void**)&devM, sizeInBytes);
cudaMalloc((void**)&devN, sizeInBytes);
// Allocate P
cudaMalloc((void**)&devP, sizeInBytes);
// Copy M and N from host to device
cudaMemcpy(devM, hostM, sizeInBytes, cudaMemcpyHostToDevice);
cudaMemcpy(devN, hostN, sizeInBytes, cudaMemcpyHostToDevice);
// Call the kernel here - Later
// Copy P matrix from device to host
cudaMemcpy(hostP, devP, sizeInBytes, cudaMemcpyDeviceToHost);
// Free allocated memory
cudaFree(devM); cudaFree(devN); cudaFree(devP);
}
Notes: Error in cudaMalloc calls: should pass address of point, e.g., “(void *)&Md”

## Slide 63: Matrix Multiply: Data Transfer
void MatrixMultiplyOnDevice(float* hostP, const float* hostM, const float* hostN, const int width)
{
int sizeInBytes = width * width * sizeof(float);
float *devM, *devN, *devP;
// Allocate M and N on device
cudaMalloc((void**)&devM, sizeInBytes);
cudaMalloc((void**)&devN, sizeInBytes);
// Allocate P
cudaMalloc((void**)&devP, sizeInBytes);
// Copy M and N from host to device
cudaMemcpy(devM, hostM, sizeInBytes, cudaMemcpyHostToDevice);
cudaMemcpy(devN, hostN, sizeInBytes, cudaMemcpyHostToDevice);
// Call the kernel here - Later
// Copy P matrix from device to host
cudaMemcpy(hostP, devP, sizeInBytes, cudaMemcpyDeviceToHost);
// Free allocated memory
cudaFree(devM); cudaFree(devN); cudaFree(devP);
}

## Slide 64: Matrix Multiply: Data Transfer
void MatrixMultiplyOnDevice(float* hostP, const float* hostM, const float* hostN, const int width)
{
int sizeInBytes = width * width * sizeof(float);
float *devM, *devN, *devP;
// Allocate M and N on device
cudaMalloc((void**)&devM, sizeInBytes);
cudaMalloc((void**)&devN, sizeInBytes);
// Allocate P
cudaMalloc((void**)&devP, sizeInBytes);
// Copy M and N from host to device
cudaMemcpy(devM, hostM, sizeInBytes, cudaMemcpyHostToDevice);
cudaMemcpy(devN, hostN, sizeInBytes, cudaMemcpyHostToDevice);
// Call the kernel here - Later
// Copy P matrix from device to host
cudaMemcpy(hostP, devP, sizeInBytes, cudaMemcpyDeviceToHost);
// Free allocated memory
cudaFree(devM); cudaFree(devN); cudaFree(devP);
}
Notes: Error in cudaMalloc calls: should pass address of point, e.g., “(void *)&Md”

## Slide 65: Matrix Multiply: Data Transfer
void MatrixMultiplyOnDevice(float* hostP, const float* hostM, const float* hostN, const int width)
{
int sizeInBytes = width * width * sizeof(float);
float *devM, *devN, *devP;
// Allocate M and N on device
cudaMalloc((void**)&devM, sizeInBytes);
cudaMalloc((void**)&devN, sizeInBytes);
// Allocate P
cudaMalloc((void**)&devP, sizeInBytes);
// Copy M and N from host to device
cudaMemcpy(devM, hostM, sizeInBytes, cudaMemcpyHostToDevice);
cudaMemcpy(devN, hostN, sizeInBytes, cudaMemcpyHostToDevice);
// Call the kernel here - Later
// Copy P matrix from device to host
cudaMemcpy(hostP, devP, sizeInBytes, cudaMemcpyDeviceToHost);
// Free allocated memory
cudaFree(devM); cudaFree(devN); cudaFree(devP);
}
Notes: Error in cudaMalloc calls: should pass address of point, e.g., “(void *)&Md”

## Slide 66: Matrix Multiply: Data Transfer
void MatrixMultiplyOnDevice(float* hostP, const float* hostM, const float* hostN, const int width)
{
int sizeInBytes = width * width * sizeof(float);
float *devM, *devN, *devP;
// Allocate M and N on device
cudaMalloc((void**)&devM, sizeInBytes);
cudaMalloc((void**)&devN, sizeInBytes);
// Allocate P
cudaMalloc((void**)&devP, sizeInBytes);
// Copy M and N from host to device
cudaMemcpy(devM, hostM, sizeInBytes, cudaMemcpyHostToDevice);
cudaMemcpy(devN, hostN, sizeInBytes, cudaMemcpyHostToDevice);
// Call the kernel here - Later
// Copy P matrix from device to host
cudaMemcpy(hostP, devP, sizeInBytes, cudaMemcpyDeviceToHost);
// Free allocated memory
cudaFree(devM); cudaFree(devN); cudaFree(devP);
}
Notes: Error in cudaMalloc calls: should pass address of point, e.g., “(void *)&Md”

## Slide 67: Matrix Multiply
Step 1:
  Add CUDA memory transfers to the skeleton
Step 2:
  Implement the kernel in CUDA C

## Slide 68: Matrix Multiply: CUDA Kernel
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
  int tx = threadIdx.x;
  int ty = threadIdx.y;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int k = 0; k < width; k++) {
    float m = devM[ty * width + k];
    float n = devN[k * width + tx];
    pValue += m * n;
  }
  // Write value to device memory - each thread has unique index to write to
  devP[ty * width + tx] = pValue;
}

## Slide 69: Matrix Multiply: CUDA Kernel
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
  int tx = threadIdx.x;
  int ty = threadIdx.y;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int k = 0; k < width; k++) {
    float m = devM[ty * width + k];
    float n = devN[k * width + tx];
    pValue += m * n;
  }
  // Write value to device memory - each thread has unique index to write to
  devP[ty * width + tx] = pValue;
}
Kernel specifier
Always void
Specify const buffers
for read-only
No const for buffers that will be written to

## Slide 70: Matrix Multiply: CUDA Kernel
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
  int tx = threadIdx.x;
  int ty = threadIdx.y;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int k = 0; k < width; k++) {
    float m = devM[ty * width + k];
    float n = devN[k * width + tx];
    pValue += m * n;
  }
  // Write value to device memory - each thread has unique index to write to
  devP[ty * width + tx] = pValue;
}
Accessing a Matrix, use 2D threads

## Slide 71: Matrix Multiply: CUDA Kernel
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
  int tx = threadIdx.x;
  int ty = threadIdx.y;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int k = 0; k < width; k++) {
    float m = devM[ty * width + k];
    float n = devN[k * width + tx];
    pValue += m * n;
  }
  // Write value to device memory - each thread has unique index to write to
  devP[ty * width + tx] = pValue;
}
Each kernel thread computes one location of the matrix

## Slide 72: Matrix Multiply: CUDA Kernel
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
  int tx = threadIdx.x;
  int ty = threadIdx.y;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int k = 0; k < width; k++) {
    float m = devM[ty * width + k];
    float n = devN[k * width + tx];
    pValue += m * n;
  }
  // Write value to device memory - each thread has unique index to write to
  devP[ty * width + tx] = pValue;
}
What happened to the 2 outer loops?

## Slide 73: Matrix Multiply: CUDA Kernel
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
  int tx = threadIdx.x;
  int ty = threadIdx.y;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int k = 0; k < width; k++) {
    float m = devM[ty * width + k];
    float n = devN[k * width + tx];
    pValue += m * n;
  }
  // Write value to device memory - each thread has unique index to write to
  devP[ty * width + tx] = pValue;
}
2D Matrix but 1D access

## Slide 74: Matrix Multiply: CUDA Kernel
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
  int tx = threadIdx.x;
  int ty = threadIdx.y;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int k = 0; k < width; k++) {
    float m = devM[ty * width + k];
    float n = devN[k * width + tx];
    pValue += m * n;
  }
  // Write value to device memory - each thread has unique index to write to
  devP[ty * width + tx] = pValue;
}
Are we missing synchronization? Why?

## Slide 75: Matrix Multiply: CUDA Kernel
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
  int tx = threadIdx.x;
  int ty = threadIdx.y;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int k = 0; k < width; k++) {
    float m = devM[ty * width + k];
    float n = devN[k * width + tx];
    pValue += m * n;
  }
  // Write value to device memory - each thread has unique index to write to
  devP[ty * width + tx] = pValue;
}
Write the value to the correct output index.

## Slide 76: Matrix Multiply
Step 1:
  Add CUDA memory transfers to the skeleton
Step 2:
  Implement the kernel in CUDA C
Step 3:
  Invoke the kernel

## Slide 77: Matrix Multiply: Invoke Kernel
// Setup thread/block execution configuration
dim3 threads(width, width);
dim3 blocks(1, 1);
// Launch the kernel
MatrixMultiplyKernel<<<blocks, threads>>>(devM, devN, devP, width)
void MatrixMultiplyOnDevice(float* hostP,
const float* hostM, const float* hostN, const int width)
{
………
// Allocate P on device
cudaMalloc((void**)&devP, sizeInBytes);
// Call the kernel here
// Copy P matrix from device to host
cudaMemcpy(hostP, devP, sizeInBytes, cudaMemcpyDeviceToHost);
………
}
Each block has (width, width) threads
Launch 1 block

## Slide 78: Matrix Multiply: Invoke Kernel
Like calling a function, but with launch configuration
// Setup thread/block execution configuration
dim3 threads(width, width);
dim3 blocks(1, 1);
// Launch the kernel
MatrixMultiplyKernel<<<blocks, threads>>>(devM, devN, devP, width)
void MatrixMultiplyOnDevice(float* hostP,
const float* hostM, const float* hostN, const int width)
{
………
// Allocate P on device
cudaMalloc((void**)&devP, sizeInBytes);
// Call the kernel here
// Copy P matrix from device to host
cudaMemcpy(hostP, devP, sizeInBytes, cudaMemcpyDeviceToHost);
………
}

## Slide 79: Matrix Multiply
What is the major performance problem with our implementation?
What is the major limitation?
What were our assumptions for this kernel?
Notes: Global memory access
Matrix size is limited by block size
We assumed a square matrix

## Slide 80: Scheduling Threads
Slide from David Luebke: http://s08.idav.ucdavis.edu/luebke-nvidia-gpu-architecture.pdf
Notes: G80 – 16 SMs, each with 8 SP.

## Slide 81: Scheduling Threads

## Slide 82: Scheduling Threads
Streaming Processor (SP)

## Slide 83: Scheduling Threads
Streaming Processors (SPs)

## Slide 84: Scheduling Threads - G80
GT80
16 SMs
Each with 8 SPs
  128 total SPs
Slide from David Luebke: http://s08.idav.ucdavis.edu/luebke-nvidia-gpu-architecture.pdf
Notes: 30 SMs * 1024 threads = 30,720 threads in flight

## Slide 85: Scheduling Threads - G80
Each SM can host: 768 Threads
Example:
6 blocks of upto 128 threads
3 blocks of 256 threads
1 block of 512 threads
Slide from David Luebke: http://s08.idav.ucdavis.edu/luebke-nvidia-gpu-architecture.pdf
Notes: 30 SMs * 1024 threads = 30,720 threads in flight

## Slide 86: Scheduling Threads - G80
In flight:
1 SM: 768 Threads
16 SMs: 16 * 768 = 12288
Slide from David Luebke: http://s08.idav.ucdavis.edu/luebke-nvidia-gpu-architecture.pdf
Notes: 30 SMs * 1024 threads = 30,720 threads in flight

## Slide 87: Scheduling Threads - GT200
GT200
30 SMs
Each with 8 SPs
  240 total SPs
Slide from David Luebke: http://s08.idav.ucdavis.edu/luebke-nvidia-gpu-architecture.pdf
Notes: 30 SMs * 1024 threads = 30,720 threads in flight

## Slide 88: Scheduling Threads - GT200
Each SM can host
8 Blocks, or
1024 Threads
Example:
8 blocks of upto 128 threads
4 blocks of 256 threads
1 block of 1024 threads
Slide from David Luebke: http://s08.idav.ucdavis.edu/luebke-nvidia-gpu-architecture.pdf
Notes: 30 SMs * 1024 threads = 30,720 threads in flight

## Slide 89: Scheduling Threads - GT200
In flight:
1 SM: 1024 Threads
30 SMs: 30 * 1024 = 30720 threads
1 SM: 8 Blocks
30 SMs: 30 * 8 = 240 Blocks
Slide from David Luebke: http://s08.idav.ucdavis.edu/luebke-nvidia-gpu-architecture.pdf
Notes: 30 SMs * 1024 threads = 30,720 threads in flight

## Slide 90: Fermi (GF110)
16 SMs
Each 32 Cores
Each SM Hosts upto
  48 warps, or
  1536 threads
In flight 24,576 threads

## Slide 91: Kepler GPU Architecture (GK110 in GTX780Ti)

## Slide 92: Kepler SMX
192 single-precision CUDA cores
64 double-precision units
32 special function units (SFU)
32 load/store units (LD/ST).
SM and SMX refer to the same hardware concept. In Kepler, NVIDIA called it Next-Gen SM or “SMX”

## Slide 96
https://developer.nvidia.com/blog/nvidia-turing-architecture-in-depth/

## Slide 98: GA102 (Ampere)
7 GPCs (Graphics Processing Clusters)
42 TPCs (Texture Processing Clusters)
84 SMs
10.752 FP32 Units
84 2nd Gen RT Cores
336 3rd Gen Tensor Cores
(RTX 3090 is not using the full GA102 - two SMs not active)

## Slide 100: Scheduling Threads
Warp – threads from a block
  32 threads
  Run on the same SM
  Unit of thread scheduling
  Consecutive threadIdx values
Notes: NVIDIA has no intention to change warp size to 32

## Slide 101: Scheduling Threads
Image from: http://bps10.idav.ucdavis.edu/talks/03-fatahalian_gpuArchTeraflop_BPS_SIGGRAPH2010.pdf
Notes: When a stall is hit, the scheduler swaps out a warp for another warp that is ready
We want to have enough blocks/warps to handle any stalls (such as reading from global memory)

## Slide 102: Scheduling Threads
Slide from: http://courses.engr.illinois.edu/ece498/al/Syllabus.html

## Slide 103: Scheduling Threads
What happens if branches in a warp diverge?

## Slide 104: Scheduling Threads
Image from: http://bps10.idav.ucdavis.edu/talks/03-fatahalian_gpuArchTeraflop_BPS_SIGGRAPH2010.pdf

## Slide 105: Scheduling Threads
An SM can host up to 1024 threads, how many warps is that?
If 3 blocks are assigned to an SM and each block has 256 threads, how many warps are there?
Notes: 1024 / 32 = 32 warps
(3 * 256) / 32 = 24 warps

## Slide 106: Scheduling Threads
Each warp has 4 multiples/adds
  16 cycles
We need to cover 200 cycles
  200 / 16 = 12.5
  ceil(12.5) = 13
13 warps are required
Notes: Our book says 14 in Section 6.4 (Data Prefetching) on Page 113, but I believe it is a typo.

## Slide 107: Memory Model Revisited

## Slide 108: Memory Model
Image from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf
Note: We will only cover registers, shared memory, global memory today

## Slide 109: Memory Model
Registers
  Per thread
  Fast, on-chip, read/write access
  Increasing the number of registers used by a kernel has what affect?
Notes: Potentially decrease the number of threads (well, blocks) available to that SM for scheduling.

## Slide 110: Memory Model - Registers
Registers – Example on G80 Architecture
  Per SM
    Up to 768 threads
    8K registers
  How many registers per thread?

## Slide 111: Memory Model - Registers
Registers - G80
  8K / 768 = 10 registers per thread
  Exceeding limit reduces threads by the block
  Example: Each thread uses 11 registers, and each block has 256 threads
    How many threads can a SM host?
    How many warps can a SM host?
    What does having less warps mean?
Notes: Host 512 threads (2 blocks instead of 3)
Host 512 / 32 = 16 warps
Instead of 768 threads and 24 warps

## Slide 112: Memory Model
Special Registers - Used for built-in variables
  threadIdx
  blockIdx
  blockDim
  gridDim

## Slide 113: Memory Model – Local Memory
Refers to memory where registers and other thread-data is spilled
  Usually when one runs out of SM resources
  “Local” because each thread has its own private area
  Arrays declared inside kernels (if compiler can’t resolve indexing)
Details:
  Not really a “memory” – bytes are stored in global memory
  Differences from global memory
    Addressing is resolved by the compiler
    Stores are cached in L1 (SM 2.x and newer)
http://developer.download.nvidia.com/CUDA/training/register_spilling.pdf

## Slide 114: Memory Model – Local Memory
It could hurt performance in two ways:
  Increased memory traffic
  Increased instruction count
Spilling/LMEM usage isn’t always bad
  LMEM bytes can get contained within L1
    Avoids memory traffic increase
  Additional instructions don’t matter much if code is not instruction-throughput limited
For performance optimization, see link below
http://developer.download.nvidia.com/CUDA/training/register_spilling.pdf

## Slide 115: Memory Model – Shared Memory
Shared Memory
  Per block
  Fast, on-chip, read/write access
  Full speed random access

## Slide 116: Memory Model – Shared Memory
Shared Memory – Example G80 Architecture
  Per SM
    Up to 8 blocks
    16 KB
  How many KB per block
Notes: 2 KB per block

## Slide 117: Memory Model – Shared Memory
Shared Memory – G80
  16 KB / 8 = 2 KB per block
  Example
    If each block uses 5 KB, how many blocks can a SM host?
Notes: 16 KB / 5 KB = 3 blocks per SM

## Slide 118: Memory Model – Global Memory
Long latency (100s cycles)
Off-chip, read/write access
Random access causes performance hit
Host can read/write
  Reads are cached (2.x and newer)
  But writes invalidate the cache
GT200
  150 GB/s
  Up to 4 GB
G80 – 86.4 GB/s
Notes: Kepler up to 200 GB/s

## Slide 119: Memory Model – Constant Memory
Constant Memory
  Short latency, high bandwidth, read only access when all threads access the same location
  Stored in global memory but cached
  Host can read/write
  Up to 64 KB

## Slide 120: Memory Model – Constant Memory
Global and constant variables
  Host can access with
    cudaGetSymbolAddress()
    cudaGetSymbolSize()
    cudaMemcpyToSymbol()
    cudaMemcpyFromSymbol()
  Constants must be declared outside of a function body
__constant__ float constData[256]; // global scope float data[256]; cudaMemcpyToSymbol(constData, data, sizeof(data)); cudaMemcpyFromSymbol(data, constData, sizeof(data));
Notes: __constant__ float constData[256];
float data[256];
cudaMemcpyToSymbol(constData, data, sizeof(data));
cudaMemcpyFromSymbol(data, constData, sizeof(data))

## Slide 121: Memory Model
Variable Declaration | Memory | Scope | Lifetime
Automatic variables other than arrays | register | thread | kernel
Automatic array variables | local | thread | kernel
__shared__ int sharedVar; | shared | block | kernel
__device__ int globalVar; | global | grid | application
__constant__ int constantVar; | constant | grid | application
See Appendix B.2 in the NVIDIA CUDA C Programming Guide for more details

## Slide 122: Thread Synchronization

## Slide 123: Thread Synchronization
Threads in a block can synchronize
  call to __syncthreads create a barrier
  A thread waits at this call until all threads in the block reach it, then all threads continue
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i + 1]);

## Slide 124: Thread Synchronization
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Time: 0
Thread 0
Thread 1
Thread 2
Thread 3
Notes: In this example, the warp size is 2. The block size is 4.

## Slide 125: Thread Synchronization
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Time: 1
Thread 0
Thread 1
Thread 2
Thread 3

## Slide 126: Thread Synchronization
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Threads 0 and 1 are blocked at barrier
Time: 1
Thread 0
Thread 1
Thread 2
Thread 3

## Slide 127: Thread Synchronization
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Time: 2
Thread 0
Thread 1
Thread 2
Thread 3

## Slide 128: Thread Synchronization
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Time: 3
Thread 0
Thread 1
Thread 2
Thread 3

## Slide 129: Thread Synchronization
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
All threads in block have reached barrier, any thread can continue
Time: 3
Thread 0
Thread 1
Thread 2
Thread 3

## Slide 130: Thread Synchronization
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Time: 4
Thread 0
Thread 1
Thread 2
Thread 3

## Slide 131: Thread Synchronization
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Time: 5
Thread 0
Thread 1
Thread 2
Thread 3

## Slide 132: Thread Synchronization
Why is it important that execution time be similar among threads?
Why does it only synchronize within a block?
Notes: Similar execution time – load balance
Synchronize within a block – runtime can schedule threads in any order

## Slide 133: Thread Synchronization
Image from http://courses.engr.illinois.edu/ece498/al/textbook/Chapter3-CudaThreadingModel.pdf

## Slide 134: Thread Synchronization
Can __syncthreads() cause a thread to hang?

## Slide 135: Thread Synchronization
if (someCondition)
{
__syncthreads();
}
// ...
Notes: Yes, if not all threads in the block execute the same condition

## Slide 136: Thread Synchronization
if (someCondition)
{
__syncthreads();
}
else
{
__syncthreads();
}
Notes: Yes, if not all threads in the block execute the same condition

## Slide 137: Let’s Revisit Matrix Multiply

## Slide 138: Matrix Multiply: CPU Implementation
Code from: http://courses.engr.illinois.edu/ece498/al/lectures/lecture3%20cuda%20threads%20spring%202010.ppt
void MatrixMultiplyOnHost(float* M, float* N, float* P, int width)‏
{
for (int i = 0; i < width; ++i)‏
{
for (int j = 0; j < width; ++j)
{
float sum = 0;
for (int k = 0; k < width; ++k)
{
float a = M[i * width + k];
float b = N[k * width + j];
sum += a * b;
}
P[i * width + j] = sum;
}
}
}
Notes: Row major. The inner most loop goes across a row of M, and down a column of N.

## Slide 139: Matrix Multiply: CUDA Kernel
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
  int tx = threadIdx.x;
  int ty = threadIdx.y;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int k = 0; k < width; k++) {
    float m = devM[ty * width + k];
    float n = devN[k * width + tx];
    pValue += m * n;
  }
  // Write value to device memory - each thread has unique index to write to
  devP[ty * width + tx] = pValue;
}

## Slide 140: Matrix Multiply: CUDA Kernel
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
  int tx = threadIdx.x;
  int ty = threadIdx.y;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int k = 0; k < width; k++) {
    float m = devM[ty * width + k];
    float n = devN[k * width + tx];
    pValue += m * n;
  }
  // Write value to device memory - each thread has unique index to write to
  devP[ty * width + tx] = pValue;
}
Kernel specifier
Always void
Specify const buffers
for read-only
No const for buffers that will be written to

## Slide 141: Matrix Multiply: CUDA Kernel
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
  int tx = threadIdx.x;
  int ty = threadIdx.y;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int k = 0; k < width; k++) {
    float m = devM[ty * width + k];
    float n = devN[k * width + tx];
    pValue += m * n;
  }
  // Write value to device memory - each thread has unique index to write to
  devP[ty * width + tx] = pValue;
}
Accessing a Matrix, use 2D threads

## Slide 142: Matrix Multiply: CUDA Kernel
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
  int tx = threadIdx.x;
  int ty = threadIdx.y;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int k = 0; k < width; k++) {
    float m = devM[ty * width + k];
    float n = devN[k * width + tx];
    pValue += m * n;
  }
  // Write value to device memory - each thread has unique index to write to
  devP[ty * width + tx] = pValue;
}
Each kernel thread computes one location of the matrix

## Slide 143: Matrix Multiply: CUDA Kernel
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
  int tx = threadIdx.x;
  int ty = threadIdx.y;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int k = 0; k < width; k++) {
    float m = devM[ty * width + k];
    float n = devN[k * width + tx];
    pValue += m * n;
  }
  // Write value to device memory - each thread has unique index to write to
  devP[ty * width + tx] = pValue;
}
What happened to the 2 outer loops?

## Slide 144: Matrix Multiply: CUDA Kernel
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
  int tx = threadIdx.x;
  int ty = threadIdx.y;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int k = 0; k < width; k++) {
    float m = devM[ty * width + k];
    float n = devN[k * width + tx];
    pValue += m * n;
  }
  // Write value to device memory - each thread has unique index to write to
  devP[ty * width + tx] = pValue;
}
2D Matrix but 1D access

## Slide 145: Matrix Multiply: CUDA Kernel
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
  int tx = threadIdx.x;
  int ty = threadIdx.y;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int k = 0; k < width; k++) {
    float m = devM[ty * width + k];
    float n = devN[k * width + tx];
    pValue += m * n;
  }
  // Write value to device memory - each thread has unique index to write to
  devP[ty * width + tx] = pValue;
}
Are we missing synchronization? Why?

## Slide 146: Matrix Multiply: CUDA Kernel
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
  int tx = threadIdx.x;
  int ty = threadIdx.y;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int k = 0; k < width; k++) {
    float m = devM[ty * width + k];
    float n = devN[k * width + tx];
    pValue += m * n;
  }
  // Write value to device memory - each thread has unique index to write to
  devP[ty * width + tx] = pValue;
}
Write the value to the correct output index.

## Slide 147: Matrix Multiply
Problems
  Limited matrix size
    Only uses one block
  Lots of global memory access

## Slide 148: Matrix Multiply
Remove size limitation
  Break Pd matrix into tiles
  Assign each tile to a block
  Use threadIdx and blockIdx for indexing
Image from http://courses.engr.illinois.edu/ece498/al/textbook/Chapter3-CudaThreadingModel.pdf

## Slide 149: Matrix Multiply
Example
  Matrix: 4x4
  TILE_WIDTH = 2
  Block size: 2x2
Image from http://courses.engr.illinois.edu/ece498/al/textbook/Chapter3-CudaThreadingModel.pdf

## Slide 150: Matrix Multiply
Pd0,0 | Pd1,0 | Pd2,0 | Pd3,0
Pd0,1 | Pd1,1 | Pd2,1 | Pd3,1
Pd0,2 | Pd1,2 | Pd2,1 | Pd3,2
Pd0,3 | Pd1,3 | Pd2,3 | Pd3,3
Example
  Matrix: 4x4
  TILE_WIDTH = 2
  Block size: 2x2
Nd0,0 | Nd1,0 | Nd2,0 | Nd3,0
Nd0,1 | Nd1,1 | Nd2,1 | Nd3,1
Nd0,2 | Nd1,2 | Nd2,1 | Nd3,2
Nd0,3 | Nd1,3 | Nd2,3 | Nd3,3
Image from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Md0,0 | Md1,0 | Md2,0 | Md3,0
Md0,1 | Md1,1 | Md2,1 | Md3,1
Md0,2 | Md1,2 | Md2,1 | Md3,2
Md0,3 | Md1,3 | Md2,3 | Md3,3
Notes: When we use tilewidth = 2, when we calculate 2x2 elements of the product matrix using a single thread

## Slide 151: Matrix Multiply
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
  int col = blockIdx.x * blockDim.x + threadIdx.x;
  int row = blockIdx.y * blockDim.y + threadIdx.y;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int k = 0; k < width; k++) {
    float m = ;
    float n = ;
    pValue += devM[row * width + k] * devN[k * width + col];
  }
  // Write value to device memory - each thread has unique index to write to
  devP[row * width + col] = pValue;
}
Code from http://courses.engr.illinois.edu/ece498/al/Syllabus.html

## Slide 152: Matrix Multiply
Code from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Calculate row index of P and M
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
  int col = blockIdx.x * blockDim.x + threadIdx.x;
  int row = blockIdx.y * blockDim.y + threadIdx.y;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int k = 0; k < width; k++) {
    float m = ;
    float n = ;
    pValue += devM[row * width + k] * devN[k * width + col];
  }
  // Write value to device memory - each thread has unique index to write to
  devP[row * width + col] = pValue;
}

## Slide 153: Matrix Multiply
Code from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
  int col = blockIdx.x * blockDim.x + threadIdx.x;
  int row = blockIdx.y * blockDim.y + threadIdx.y;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int k = 0; k < width; k++) {
    float m = ;
    float n = ;
    pValue += devM[row * width + k] * devN[k * width + col];
  }
  // Write value to device memory - each thread has unique index to write to
  devP[row * width + col] = pValue;
}
Calculate col index of P and N

## Slide 154: Matrix Multiply
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
  int col = blockIdx.x * blockDim.x + threadIdx.x;
  int row = blockIdx.y * blockDim.y + threadIdx.y;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int k = 0; k < width; k++) {
    float m = ;
    float n = ;
    pValue += devM[row * width + k] * devN[k * width + col];
  }
  // Write value to device memory - each thread has unique index to write to
  devP[row * width + col] = pValue;
}
Code from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Each thread computes 1 element of P sub-matrix

## Slide 155: Matrix Multiply
Code from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Write value to devP
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
  int col = blockIdx.x * blockDim.x + threadIdx.x;
  int row = blockIdx.y * blockDim.y + threadIdx.y;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int k = 0; k < width; k++) {
    float m = ;
    float n = ;
    pValue += devM[row * width + k] * devN[k * width + col];
  }
  // Write value to device memory - each thread has unique index to write to
  devP[row * width + col] = pValue;
}

## Slide 156: Matrix Multiply: Invoke Kernel
// Setup thread/block execution configuration
dim3 dimBlocks(TILE_WIDTH, TILE_WIDTH);
dim3 dimGrid(WIDTH / TILE_WIDTH, WIDTH / TILE_WIDTH);
// Launch the kernel
MatrixMultiplyKernel<<<dimGrid, dimBlocks>>>(devM, devN, devP, width);
void MatrixMultiplyOnDevice(float* hostP,
const float* hostM, const float* hostN, const int width)
{
………
// Allocate P on device
cudaMalloc((void**)&devP, sizeInBytes);
// Call the kernel here
// Copy P matrix from device to host
cudaMemcpy(hostP, devP, sizeInBytes, cudaMemcpyDeviceToHost);
………
}
Launch multiple block
Each block has (width, width) threads

## Slide 157: What about global memory access?

## Slide 158: Matrix Multiply
Limited by global memory bandwidth
  G80 peak GFLOPS: 346.5
  Require 1386 GB/s to achieve this
  G80 memory bandwidth: 86.4 GB/s
    Limits code to 21.6 GFLOPS
    In practice, code runs at 15 GFLOPS
  Must drastically reduce global memory access

## Slide 159: Matrix Multiply
Each input element is read by Width threads
Use shared memory to reduce global memory bandwidth
Image from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
M
N
P
WIDTH
WIDTH
WIDTH
WIDTH
ty
tx

## Slide 160: Matrix Multiply
Break kernel into phases
  Each phase accumulates Pd using a subset of Md and Nd
  Each phase has good data locality
Image from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Md
Nd
Pd
Width
Width
Width
Width
Tile
Width
Tile
Width
Tile
Width
Tile
Width
Tile
Width
Tile
Width
1
0
2
1
0
2
BY
BX
0 1 2 TILE_WIDTH - 1
0
1
2
TILE_WIDTH - 1
TX
TY

## Slide 161: Matrix Multiply
Each thread
  loads one element of Md and Nd in the tile into shared memory
Image from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Md
Nd
Pd
Width
Width
Width
Width
Tile
Width
Tile
Width
Tile
Width
Tile
Width
Tile
Width
Tile
Width
1
0
2
1
0
2
BY
BX
0 1 2 TILE_WIDTH - 1
0
1
2
TILE_WIDTH - 1
TX
TY
m
by
bx
m
k
k

## Slide 162
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
__shared__ float sM[TILE_WIDTH][TILE_WIDTH];
__shared__ float sN[TILE_WIDTH][TILE_WIDTH];
int bx = blockIdx.x; int by = blockIdx.y;
int tx = threadIdx.x; int ty = threadIdx.y;
  int col = bx * TILE_WIDTH + tx;
  int row = by * TILE_WIDTH + ty;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int m = 0; m < width / TILE_WIDTH; m++) {
sM[ty][tx] = devM[row * width + (m * TILE_WIDTH + tx)];
sN[ty][tx] = devN[col + (m * TILE_WIDTH + ty) * Width];
__syncthreads();
for (int k = 0; k < TILE_WIDTH; ++k)
Pvalue += sM[ty][k] * sN[k][tx];
__synchthreads();
}
devP[row * width + col] = pValue;
}
Code from http://courses.engr.illinois.edu/ece498/al/Syllabus.html

## Slide 163
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
__shared__ float sM[TILE_WIDTH][TILE_WIDTH];
__shared__ float sN[TILE_WIDTH][TILE_WIDTH];
int bx = blockIdx.x; int by = blockIdx.y;
int tx = threadIdx.x; int ty = threadIdx.y;
  int col = bx * TILE_WIDTH + tx;
  int row = by * TILE_WIDTH + ty;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int m = 0; m < width / TILE_WIDTH; m++) {
sM[ty][tx] = devM[row * width + (m * TILE_WIDTH + tx)];
sN[ty][tx] = devN[col + (m * TILE_WIDTH + ty) * Width];
__syncthreads();
for (int k = 0; k < TILE_WIDTH; ++k)
Pvalue += sM[ty][k] * sN[k][tx];
__synchthreads();
}
devP[row * width + col] = pValue;
}
Code from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Shared memory of M and N submatrices

## Slide 164
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
__shared__ float sM[TILE_WIDTH][TILE_WIDTH];
__shared__ float sN[TILE_WIDTH][TILE_WIDTH];
int bx = blockIdx.x; int by = blockIdx.y;
int tx = threadIdx.x; int ty = threadIdx.y;
  int col = bx * TILE_WIDTH + tx;
  int row = by * TILE_WIDTH + ty;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int m = 0; m < width / TILE_WIDTH; m++) {
sM[ty][tx] = devM[row * width + (m * TILE_WIDTH + tx)];
sN[ty][tx] = devN[col + (m * TILE_WIDTH + ty) * Width];
__syncthreads();
for (int k = 0; k < TILE_WIDTH; ++k)
Pvalue += sM[ty][k] * sN[k][tx];
__synchthreads();
}
devP[row * width + col] = pValue;
}
Code from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Store blockIdx/ThreadIdx before calculating row and col

## Slide 165
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
__shared__ float sM[TILE_WIDTH][TILE_WIDTH];
__shared__ float sN[TILE_WIDTH][TILE_WIDTH];
int bx = blockIdx.x; int by = blockIdx.y;
int tx = threadIdx.x; int ty = threadIdx.y;
  int col = bx * TILE_WIDTH + tx;
  int row = by * TILE_WIDTH + ty;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int m = 0; m < width / TILE_WIDTH; m++) {
sM[ty][tx] = devM[row * width + (m * TILE_WIDTH + tx)];
sN[ty][tx] = devN[col + (m * TILE_WIDTH + ty) * Width];
__syncthreads();
for (int k = 0; k < TILE_WIDTH; ++k)
Pvalue += sM[ty][k] * sN[k][tx];
__synchthreads();
}
devP[row * width + col] = pValue;
}
Code from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
m is index of current phase
This is the number of phases to iterate

## Slide 166
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
__shared__ float sM[TILE_WIDTH][TILE_WIDTH];
__shared__ float sN[TILE_WIDTH][TILE_WIDTH];
int bx = blockIdx.x; int by = blockIdx.y;
int tx = threadIdx.x; int ty = threadIdx.y;
  int col = bx * TILE_WIDTH + tx;
  int row = by * TILE_WIDTH + ty;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int m = 0; m < width / TILE_WIDTH; m++) {
sM[ty][tx] = devM[row * width + (m * TILE_WIDTH + tx)];
sN[ty][tx] = devN[col + (m * TILE_WIDTH + ty) * Width];
__syncthreads();
for (int k = 0; k < TILE_WIDTH; ++k)
Pvalue += sM[ty][k] * sN[k][tx];
__synchthreads();
}
devP[row * width + col] = pValue;
}
Code from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Bring one element from each devM and devN into shared memory

## Slide 167
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
__shared__ float sM[TILE_WIDTH][TILE_WIDTH];
__shared__ float sN[TILE_WIDTH][TILE_WIDTH];
int bx = blockIdx.x; int by = blockIdx.y;
int tx = threadIdx.x; int ty = threadIdx.y;
  int col = bx * TILE_WIDTH + tx;
  int row = by * TILE_WIDTH + ty;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int m = 0; m < width / TILE_WIDTH; m++) {
sM[ty][tx] = devM[row * width + (m * TILE_WIDTH + tx)];
sN[ty][tx] = devN[col + (m * TILE_WIDTH + ty) * Width];
__syncthreads();
for (int k = 0; k < TILE_WIDTH; ++k)
pValue += sM[ty][k] * sN[k][tx];
__synchthreads();
}
devP[row * width + col] = pValue;
}
Code from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Accumulate subset of dot product

## Slide 168
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
__shared__ float sM[TILE_WIDTH][TILE_WIDTH];
__shared__ float sN[TILE_WIDTH][TILE_WIDTH];
int bx = blockIdx.x; int by = blockIdx.y;
int tx = threadIdx.x; int ty = threadIdx.y;
  int col = bx * TILE_WIDTH + tx;
  int row = by * TILE_WIDTH + ty;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int m = 0; m < width / TILE_WIDTH; m++) {
sM[ty][tx] = devM[row * width + (m * TILE_WIDTH + tx)];
sN[ty][tx] = devN[col + (m * TILE_WIDTH + ty) * Width];
__syncthreads();
for (int k = 0; k < TILE_WIDTH; ++k)
pValue += sM[ty][k] * sN[k][tx];
__synchthreads();
}
devP[row * width + col] = pValue;
}
Code from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Why
Notes: Need to sync the entire block after write

## Slide 169
__global__ void MatrixMultiplyKernel(const float* devM, const float* devN,
float* devP, const int width)
{
__shared__ float sM[TILE_WIDTH][TILE_WIDTH];
__shared__ float sN[TILE_WIDTH][TILE_WIDTH];
int bx = blockIdx.x; int by = blockIdx.y;
int tx = threadIdx.x; int ty = threadIdx.y;
  int col = bx * TILE_WIDTH + tx;
  int row = by * TILE_WIDTH + ty;
  // Initialize accumulator to 0
  float pValue = 0;
  // Multiply and add
  for (int m = 0; m < width / TILE_WIDTH; m++) {
sM[ty][tx] = devM[row * width + (m * TILE_WIDTH + tx)];
sN[ty][tx] = devN[col + (m * TILE_WIDTH + ty) * Width];
__syncthreads();
for (int k = 0; k < TILE_WIDTH; ++k)
pValue += sM[ty][k] * sN[k][tx];
__synchthreads();
}
devP[row * width + col] = pValue;
}
Code from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Write final answer to global memory
Notes: Need to sync the entire block after write

## Slide 170: Matrix Multiply
How do you pick TILE_WIDTH?
How can it be too large?

## Slide 171: Matrix Multiply
How do you pick TILE_WIDTH?
How can it be too large?
  By exceeding the maximum number of threads/block

## Slide 172: Matrix Multiply
How do you pick TILE_WIDTH?
How can it be too large?
  By exceeding the maximum number of threads/block
  By exceeding the shared memory limitations
    G80: 16KB per SM and up to 8 blocks per SM
      2 KB per block
      1 KB for Nds and 1 KB for Mds (16 * 16 * 4)
      TILE_WIDTH = 16
      A larger TILE_WIDTH will result in less blocks

## Slide 173: Matrix Multiply
Shared memory tiling benefits
  Reduces global memory access by a factor of TILE_WIDTH
    16x16 tiles reduces by a factor of 16
  G80
    Now global memory supports 345.6 GFLOPS
    Close to maximum of 346.5 GFLOPS

## Slide 174: Math Functions
double and float overloads
On the host, functions use the C runtime implementation if available
https://docs.nvidia.com/cuda/cuda-math-api/index.html
Notes: On the device, SFU are likely used.

## Slide 175: Math Functions
Partial list:
  sqrt, rsqrt
  exp, log
  sin, cos, tan, sincos
  asin, acos, atan2
  trunc, ceil, floor
https://docs.nvidia.com/cuda/cuda-math-api/group__CUDA__MATH__SINGLE.html#group__CUDA__MATH__SINGLE

## Slide 176: Math Functions
Intrinsic function
  Device only
  Faster, but less accurate
  Prefixed with __ (double underscore)
  __exp, __log, __sin, __pow, …
https://docs.nvidia.com/cuda/cuda-math-api/group__CUDA__MATH__INTRINSIC__SINGLE.html#group__CUDA__MATH__INTRINSIC__SINGLE

## Slide 177: Vector Types
char[1–4], uchar[1–4]
short[1–4], ushort[1–4]
int[1–4], uint[1–4]
long[1–4], ulong[1–4]
longlong[1–4], ulonglong[1–4]
float[1–4]
double1, double2
Notes: Notes for 2019: Move vector types to different slide deck

## Slide 178: Vector Types
Available in host and device code
Construct with make_<type name>
Vector types (float4) are faster than regular static arrays (float [4])
int2 i2 = make_int2(1, 2);
float4 f4 = make_float4(1.0f, 2.0f, 3.0f, 4.0f);
Notes: Vector types are faster because the compiler can better optimize memory operations

## Slide 179: Vector Types
Access with .x, .y, .z, and .w
int2 i2 = make_int2(1, 2);
int x = i2.x;
int y = i2.y;

## Slide 180: CUDA Libraries
https://developer.nvidia.com/gpu-accelerated-libraries

## Slide 181: CUDA Libraries – NVIDIA CUDA-X
NVIDIA CUDA-X - collection of libraries for multiple application domains, from artificial intelligence (AI) to high performance computing (HPC).
Math, Algorithms, Image and Video, Deep Learning…
Get the most optimized algorithms
  Optimized by experts
  No need to write any kernel
https://developer.nvidia.com/gpu-accelerated-libraries

## Slide 182: CUDA Libraries
How many of you have used a library like:
  BLAS (OpenBLAS etc)
  FFTW
  LAPACK
  Intel MKL
  FFMPEG

## Slide 183: CUDA Libraries
cuBLAS – GPU accelerated BLAS
cuFFT – GPU accelerated FFT
cuSOLVER – dense and sparse solvers
cuSPARSE – BLAS for sparse
cuTENSOR – Tensor linear algebra library
CUDA Math – GPU math functions
cuDNN – Library of primitives for deep neural networks
TensorRT – Inference optimizer and runtime deployment
DALI – Decoding and augmenting images and videos
(Not exhaustive list)

## Slide 184: Thrust

## Slide 185: What is Thrust?
Open source High-Level Parallel Algorithms Library
Parallel Analog of the C++ Standard Template Library (STL)
Performance-Portable Abstraction Layer
Productive way to program CUDA
http://developer.download.nvidia.com/compute/developertrainingmaterials/presentations/cuda_language/Introduction_to_Thrust.pptx

## Slide 186: For a review of C++ STL and Thrust Similarities, see: http://cs.boisestate.edu/~alark/thrust_intro/presentation.html#slide1

## Slide 187: Example - Sort
#include <thrust/host_vector.h>
#include <thrust/device_vector.h>
#include <thrust/sort.h>
#include <cstdlib>
int main(void)
{
// generate 32M random numbers on the host
thrust::host_vector<int> h_vec(32 << 20);
thrust::generate(h_vec.begin(), h_vec.end(), rand);
// transfer data to the device
thrust::device_vector<int> d_vec = h_vec;
// sort data on the device
thrust::sort(d_vec.begin(), d_vec.end());
// transfer data back to host
thrust::copy(d_vec.begin(), d_vec.end(), h_vec.begin());
return 0;
}
http://developer.download.nvidia.com/compute/developertrainingmaterials/presentations/cuda_language/Introduction_to_Thrust.pptx

## Slide 188: Example - Reduce
#include <thrust/host_vector.h>
#include <thrust/device_vector.h>
#include <thrust/generate.h>
#include <thrust/reduce.h>
#include <thrust/functional.h>
#include <algorithm>
#include <cstdlib>
int main(void)
{
// generate random data serially
thrust::host_vector<int> h_vec(100);
std::generate(h_vec.begin(), h_vec.end(), rand);
// transfer to device and compute sum
thrust::device_vector<int> d_vec = h_vec;
int x = thrust::reduce(d_vec.begin(), d_vec.end(), 0, thrust::plus<int>());
return 0;
}
http://developer.download.nvidia.com/compute/developertrainingmaterials/presentations/cuda_language/Introduction_to_Thrust.pptx

## Slide 189: Easy to Use
Distributed with CUDA Toolkit
Header-only library
Architecture agnostic
Just compile and run!
$ nvcc -O2 -arch=sm_20 program.cu -o program
http://developer.download.nvidia.com/compute/developertrainingmaterials/presentations/cuda_language/Introduction_to_Thrust.pptx

## Slide 190: Why should I use Thrust?

## Slide 191: Productivity
Containers
  host_vector
  device_vector
Memory Management
  Allocation
  Transfers
Algorithm Selection
  Location is implicit
// allocate host vector with two elements
thrust::host_vector<int> h_vec(2);
// copy host data to device memory
thrust::device_vector<int> d_vec = h_vec;
// write device values from the host
d_vec[0] = 27;
d_vec[1] = 13;
// read device values from the host
int sum = d_vec[0] + d_vec[1];
// invoke algorithm on device
thrust::sort(d_vec.begin(), d_vec.end());
// memory automatically released
http://developer.download.nvidia.com/compute/developertrainingmaterials/presentations/cuda_language/Introduction_to_Thrust.pptx

## Slide 192: Thrust - Memory
With raw CUDA, you have to deal with a lot of low-level memory management.
With Thrust, let the library do the work for you.
http://cs.boisestate.edu/~alark/thrust_intro/presentation.html#slide17
cudaMalloc(void ** devPtr, size_t size);
cudaMemcpy(void * dst, void * src, size_t size, direction);
cudaFree(void * devPtr);
// ...
thrust::host_vector<int> h_nums(1024);
thrust::device_vector<int> d_nums;
// copy from host to device
d_nums = h_nums; // calls cudaMemcpy in background
// do some number crunching on the GPU…
// copy from device to host
h_nums = d_nums;

## Slide 193: Productivity
Large set of algorithms
  ~75 functions
  ~125 variations
Flexible
  User-defined types
  User-defined operators
Algorithm | Description
reduce | Sum of a sequence
find | First position of a value in a sequence
mismatch | First position where two sequences differ
inner_product | Dot product of two sequences
equal | Whether two sequences are equal
min_element | Position of the smallest value
count | Number of instances of a value
is_sorted | Whether sequence is in sorted order
transform_reduce | Sum of transformed sequence
http://developer.download.nvidia.com/compute/developertrainingmaterials/presentations/cuda_language/Introduction_to_Thrust.pptx

## Slide 194: Thurst – Template Algorithms
With raw CUDA, you have to manage
  Grid and Block dimensions
  Optimal launch parameters for hardware
  Other memory and related factors
// call some device code
add_some_vectors<<<dim3 gridSize, dim3 blockSize>>>(
int *in1, int *in2, int *out
);

## Slide 195: Thurst – Template Algorithms
With Thrust, use template algorithms!
  Logic for grid/block dimensions is contained in the library, so let it make smart guesses on what to use.
thrust::device_vector<int> d_src1, d_src2, d_dst;
thrust::transform(d_src1.begin(), d_src1.end(),
d_src2.begin(),
d_dst.begin(),
addFunc); // functor!

## Slide 196: Thurst – Template Algorithms
Many built-in algorithms to use on the GPU
Most of the algorithms are modeled after the STL algorithms for familiarity.
thrust::find(begin, end, value);
thrust::find_if(begin, end, Predicate);
thrust::copy(src_begin, src_end, dst_begin);
thrust::copy_if(src_begin, src_end, dst_begin, Predicate);
thrust::count(begin, end, value);
thrust::count_if(begin, end, Predicate);
thrust::equal(src1_begin, src1_end, src2_begin);
thrust::min_element(begin, end, [Cmp])
thrust::max_element(begin, end, [Cmp])
thrust::merge(src1_begin, src1_end, src2_begin, src2_end, dst_begin);
thrust::sort(begin, end, [Cmp])
// Map/Reduce (transform === map)
thrust::transform(src1_begin, src1_end, src2_begin,
dst_begin, BinaryOp);
thrust::reduce(begin, end, init, BinaryOp);
// ... and many more ...

## Slide 197: Interoperability
Thrust
CUDA C/C++
CUBLAS, CUFFT, NPP
STL
CUDA Fortran
C/C++
OpenMP
TBB
http://developer.download.nvidia.com/compute/developertrainingmaterials/presentations/cuda_language/Introduction_to_Thrust.pptx

## Slide 198: Portability
Support for CUDA, TBB and OpenMP
  Just recompile!
GeForce GTX 280
$ time ./monte_carlo
pi is approximately 3.14159
real 0m6.190s
user 0m6.052s
sys 0m0.116s
NVIDA GeForce GTX 580
Core2 Quad Q6600
$ time ./monte_carlo
pi is approximately 3.14159
real 1m26.217s
user 11m28.383s
sys 0m0.020s
Intel Core i7 2600K
nvcc -DTHRUST_DEVICE_SYSTEM=THRUST_HOST_SYSTEM_OMP
http://developer.download.nvidia.com/compute/developertrainingmaterials/presentations/cuda_language/Introduction_to_Thrust.pptx

## Slide 199: Backend System Options
Device Systems
THRUST_DEVICE_SYSTEM_CUDA
THRUST_DEVICE_SYSTEM_OMP
THRUST_DEVICE_SYSTEM_TBB
Host Systems
THRUST_HOST_SYSTEM_CPP
THRUST_HOST_SYSTEM_OMP
THRUST_HOST_SYSTEM_TBB
http://developer.download.nvidia.com/compute/developertrainingmaterials/presentations/cuda_language/Introduction_to_Thrust.pptx

## Slide 200: Multiple Backend Systems
Mix different backends freely within the same app
thrust::omp::vector<float> my_omp_vec(100);
thrust::cuda::vector<float> my_cuda_vec(100);
...
// reduce in parallel on the CPU
thrust::reduce(my_omp_vec.begin(), my_omp_vec.end());
// sort in parallel on the GPU
thrust::sort(my_cuda_vec.begin(), my_cuda_vec.end());
http://developer.download.nvidia.com/compute/developertrainingmaterials/presentations/cuda_language/Introduction_to_Thrust.pptx

## Slide 201: Performance Portability
Sort
Radix Sort
G80
GT200
Fermi
Kepler
Merge Sort
G80
GT200
Fermi
Kepler
Thrust
CUDA
OpenMP
Transform
Sort
Reduce
Transform
Sort
Reduce
Scan
Scan
http://developer.download.nvidia.com/compute/developertrainingmaterials/presentations/cuda_language/Introduction_to_Thrust.pptx

## Slide 202: Other Thrust Goodness - Functors
// calculate result[] = (a * x[]) + y[]
struct saxpy {
const float _a;
saxpy(int a) : _a(a) { }
__host__ __device__
float operator()(const float &x, const float& y) const {
return a * x + y;
}
};
thrust::device_vector<float> x, y, result;
// ... fill up x & y vectors ...
thrust::transform(x.begin(), x.end(), y.begin(),
result.begin(), saxpy(a));
Functors – give your own custom functors to kernels to run; Examples:
  Custom transforms - SAXPY
  Custom sorting conditions
  Copy-if/Count-if/Remove-if
  Custom equals
Works on both Host and Device

## Slide 203: Other Thrust Goodness – Fancy Iterators
// continually returns a constant value
thrust::constant_iterator
// provides a counter - useful for getting index
thrust::counting_iterator
// zip together multiple iterators to pass more arguments
thrust::zip_iterator
STL-like Fancy and Custom Iterators
  Custom transforms - SAXPY
  Custom sorting conditions
  Copy-if/Count-if/Remove-if
  Custom equals
thrust::device_vector<int> d1(65536);
// the for loop below is OK for quick debugging,
// but is obnoxiously slow - Why?
for (int i=0; i<d1.size(); ++i) {
std::cout << d1[i] << std::endl;
}
// there are d1.size() cudaMemcpy calls being made!
// it is usually better to copy the whole vector or
// decent sized chunks into host_vectors first
thrust::host_vector<int> h1(d1); // one cudaMemcpy
thrust::host_vector<int> h2(d1.begin(), d1.begin()+512);
for (int i=0; i<h1.size(); ++i) {
std::cout << h1[i] << std::endl;
}

## Slide 204: Robustness
Reliable
  Supports all CUDA-capable GPUs
Well-tested
  ~850 unit tests run daily
Robust
  Handles many pathological use cases
http://developer.download.nvidia.com/compute/developertrainingmaterials/presentations/cuda_language/Introduction_to_Thrust.pptx

## Slide 205: Thrust Conclusion
Thrust offers a high degree of portability and flexibility
  Easy to get started, write parallel code and to read
Robust, optimized algorithms at your fingertips
Re-use vs Re-build – Prefer re-use
Can always fallback to raw CUDA for custom tasks

## Slide 206
Other GPU Accelerated Libraries to Consider

## Slide 207: Recap and Conclusion

## Slide 208: Recap
CUDA is great for massively parallel programming
  SIMD – “Single Instruction Multiple Data”
Need enough compute to cover memory overhead
Start naïve, then optimize
Be smart about asynchronous ops and memory

## Slide 209: What we haven’t covered
Detailed GPU Architecture
Parallelizing Algorithms
Performance optimization
  Warp partitioning
  Memory coalescing
  Shared mem bank conflicts
CUDA Atomics
Advance Memory Ops
Streams
Compute-Copy Overlap
Tools
  NVIDIA Nsight Debugger
  Compute Profiler
And much more……

## Slide 210: Resources
CUDA C Programming Guide
NVIDIA Nsight
Programming Massively Parallel Processors
NVIDIA GTC On-Demand
Thrust
Penn CIS 565
Intro to Parallel Programming CUDA - Udacity
CUDA Education

## Slide 211: Pop Quiz

## Slide 212: List a few differences between CPU and GPU

## Slide 213
https://www10.mcadcafe.com/blogs/jeffrowe/2017/03/16/the-continuing-importance-of-gpus-for-more-than-just-pretty-pictures/

## Slide 214: What are the terms for CPU and GPU used in CUDA?

## Slide 215: Heterogenous Computing - Terminology
Host: typically, the CPU
  Code written in C/C++ (or other languages)
Device: typically, the GPU (data-parallel)
  Code written in extended C/C++
Host and device have separate memories
  Except for SoC
CUDA Program
  Contains both host and device code
Host
Device

## Slide 216: What is the data parallel function in CUDA called?

## Slide 217: Heterogenous Computing - Terminology
Kernel: data parallel function
  Invoking a kernel creates lightweight threads on the device
  Threads are generated and scheduled with hardware
Serial Code
Parallel Code
Serial Code

## Slide 218: What is specifier for a kernel?

## Slide 219: CUDA Kernels
Executed N times in parallel by N different CUDA threads
// Kernel Definition
__global__ void vectorAdd(const float* A, const float* B, float* C)
Declaration specifier
Notes: threadIdx is a 3-component vector

## Slide 220: What are the levels of logical constructs for parallelism?

## Slide 221: Thread Hierarchies

## Slide 222: Thread Hierarchies
Grid – one or more thread blocks
  1D, 2D or 3D
Block – array of threads
  1D, 2D, or 3D
  Each block in a grid has the same number of threads
  Each thread in a block can
    Synchronize
    Access shared memory

## Slide 223: How many threads in a block?

## Slide 224: 1024

## Slide 225: What can threads in a block do that blocks in a grid can’t do?

## Slide 226: Thread Hierarchies
Image from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf

## Slide 227: What are the different types of memory on a GPU?

## Slide 228: CUDA Memory Transfers
Image from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf

## Slide 229: What are the built-in variables in CUDA for determining thread ID information?

## Slide 230
threadIdx - Index of thread in a block
blockIdx - Index of block in a grid
blockDim - Size of block (No. of threads in a block)
gridDim - Size of grid (No. of blocks in a grid)

## Slide 231: What are the ranges of threadIdx and blockIdx?

## Slide 232
Range of threadIdx
threadIdx.x = [0, blockDim.x - 1]
threadIdx.y = [0, blockDim.y - 1]
threadIdx.z = [0, blockDim.z - 1]
Range of blockIdx
blockIdx.x = [0, gridDim.x - 1]
blockIdx.y = [0, gridDim.y - 1]
blockIdx.z = [0, gridDim.z - 1]

## Slide 233: How to calculate globally unique thread index for 2D block in a 2D grid?

## Slide 234: Thread Hierarchies
// Kernel Definition
__global__ void matrixAddition(const float* A, const float* B, float* C,
int N)
{
int x = blockIdx.x * blockDim.x + threadIdx.x;
int y = blockIdx.y * blockDim.y + threadIdx.y;
int idx = y * N + x;
C[idx] = A[idx] + B[idx];
}
int main()
{
// ....
// Kernel invocation with computed configuration
dim3 threadsPerBlock(16, 16);
dim3 blocks(N / threadPerBlock.x, N / threadPerBlock.y);
vectorAdd<<<blocks, threadsPerBlock>>>(A, B, C);
}
2D Thread Index to 1D memory index
2D grid of blocks
2D block of threads
16x16 Threads per Block
Notes: dim3 default argument is 1

## Slide 235: What are the 3 basic CUDA memory API?

## Slide 236: CUDA Memory Transfers
cudaMalloc()
  Allocate global memory on device
cudaFree()
  Frees memory
cudaMemcpy()
  Copy memory
Image from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf

## Slide 237: What are the different direction of memory copy using CUDA API?

## Slide 238: CUDA Memory Transfers
cudaMemcpy() - Memory transfer
  Host to host
  Host to device
  Device to host
  Device to device
Host
Device
Global Memory
cudaMemcpy(destPtr, sourcePtr, size cudaMemcpyDeviceToHost);
Destination
Source
Copy direction

## Slide 239: Pop Quiz for me?